## Slide 1
RAMAN SPECTROSCOPY
-An Introductory lecture

## Slide 2
Sir. C.V. Raman discovered light scattering in 1928
Awarded Nobel Prize in physics in 1930
Experiment composed of light source (sunlight), a sample, and detector (eye)
History

## Slide 3
Spectroscopic technique – observes rotational, vibrational and other low frequency modes in a system.
Complementary to IR spectroscopic technique.
Inelastic scattering or Raman scattering of monochromatic light
Introduction

## Slide 4
Laser in the visible, near IR and near UV range is used.
Interaction with molecular vibrations – energy of laser photons shifted - the change in energy of the light is measured.
Photons are not absorbed – the energy shift of the incident light indicates presence of characteristic vibrations in the molecule.
Basic principle

## Slide 5
Raman Basics – Selection rule
Excitation of the molecule to a virtual energy state .
Relaxation – energy difference is equal to the energy difference of the new state and the original state of the molecule.
Raman active – molecular polarization potential must change – deformation of electron cloud.
Amount of polarizability change – determines Raman intensity – Differential scattering cross section
Raman scattering intensity is of the order of 107 to 10 15 times weaker than the incident photon.
Wavenumber (cm1)
105 times stronger than Raman scattering

## Slide 6
Raman shifts can be expressed as o ± m
Raman Basics
Raman shifts are measured in wavenumbers (cm-1)
Stokes and Anti-stokes produce same spectrum, differing in intensity.
Intensity is governed by the
Maxwell-Boltzmann Distribution law
Stokes and Anti-stokes Raman Spectrum of CCl4

## Slide 7
Raman Spectrum

## Slide 8
IR and Raman
Spectra of PETN
explosive

## Slide 9
IR and Raman
The polarizability and electric field – tensor quantity.
Any of the component of the
polarizability tensor changes -
vibration is Raman active .
Shape, size or orientation of polarizability ellipsoid changes – vibration is Raman active
Shape change – diagonal elements
Orientation change – off-diagonal elements are changing

## Slide 10
IR and Raman
IR
Raman
Change of polarizability ellipsoid of H2O molecule during each normal mode of vibration
Molecule – center of symmetry – Vibrations are Raman active and IR inactive – the mutual exclusion principle.

## Slide 11
Raman – Advantages and Disadvantages
Provides information on vibrational frequencies of a molecule.
Totally symmetric vibrations are always Raman active – mutual exclusion principle – Both Raman and IR active
Covalent bonds are strong in Raman while ionic bonds are strong in IR
Bending vibrations are weaker than stretching in Raman.
Laser beam diameter 1-2mm – very small sample area is used in Raman
Water – no interference in Raman – easy to measure biological samples.
Instrument – expensive – laser source – heating, photodecomposition and fluorescence.

## Slide 12
Instrumentation
Excitation source – CW Laser or pulsed laser
Sample illumination and collection system
Wavelength selector
Detection and processing system

## Slide 13
Instrumental components
Laser wavelengths ranging from ultra-violet through visible to near infra-red can be used for Raman spectroscopy.
Typical examples include:
Ultra-violet: 244 nm, 257 nm, 325 nm, 364 nm
Visible: 457 nm, 473 nm, 488 nm, 514 nm, 532 nm, 633 nm, 660 nm
Near infra-red: 785 nm, 830 nm, 980 nm, 1064 nm
CW laser: early gas laser Ar+ , Kr+
Pulsed laser: Nd-YAG, diode, excimer laser.

## Slide 14
Effect of Laser source
Spectrum of Anthracene
A: Ar+ Laser (514nm)
B: Nd-YAG (1064nm)
Better to use short wavelength (4th power dependence) but long wavelength to avoid fluorescence

## Slide 15
Instrumental components
Sample illumination:
Since very weak intensity of scattering peaks –
90 geometry b) 180 geometry
Collection optics – achromatic lens system with a collecting and a focusing lens.
Wavelength selector – interference filter – monochromator – grating
Detector – detection and amplification – photon counting – photo diode array – Charge coupled devices

## Slide 16
FT-Raman
Optical diagram of FT- Raman spectrometer
Interferometer – optical filter to reduce stray light and Rayleigh line.

## Slide 17
FT-Raman
Will not completely eliminate fluorescence – NIR absorption poses problem for transition metals
Can not displace dispersive Raman
Can not detect ppm concentrations
Above 150 temp. thermal blackbody radiation from sample causes problem – more intense than Raman signal – detector gets saturated.

## Slide 18
https://www.youtube.com/watch?v=57hRNhefXPg
https://www.youtube.com/watch?v=hue2TrYXY54